## Slide 1: ECE 478-578 Intelligent Robotics I
PhD. Husnu Melih Erdogan – Electrical & Computer Engineering
herdogan@pdx.edu Teaching Assistant – Lab Assistant

## Slide 2: Dynamixel

## Slide 3: How to Setup Dynamixel Servos

## Slide 4: USB2Dyanmixel Adaptor

## Slide 5: Power Hub

## Slide 6: Dyanmixel Servos
Dynamixel actuators have been used by every major university, research lab, military & government research lab, and robotic competition worldwide.
The casing of each servo is built specifically with robotics in mind, providing easy to use mounting rails and a comprehensive bracket system available for building robotic limbs.
TTL and RS-485 serial communication allows for daisy-chainable bus connections at up to 1-3mbps.

## Slide 7
http://www.pitt.edu/~sorc/robotics/handbook/ServoControl.htm
http://www.pyroelectro.com/tutorials/servo_motor/servomotor.html
Conventional Servo motors are used for positioning
  every 20ms you need to send a pulse to the servo motor,
  the width of this pulse determines the position the servo.
This has to be done for every servo motor in the system => large overhead on main mcu.
How Regular Servos Work

## Slide 8
        Use serial communication:
          TTL serial (3 wire) or RS485 (4 wire), and
          1Mbps to 3Mbps communication speeds.
http://tribotix.com/Products/Robotis/Dynamixel/DynamixelIntro.htm
        Dynamixels are ‘networked’:
          each Dynamixel in the chain must have a unique ID
          they are connected via a Daisy Chain, and
          255 Dynamixels can be connected to each network.
How Dynamixel Servos Work
Dynamixels are driven by digital packet communication. The main communication protocol is half-duplex UART (8-bit, no parity, 1 stop).
It supports TTL, RS485, or CAN networks. Dynamixel communicates with the main controller by sending and receiving packets of data on a bus.

## Slide 9
Basic Setup for Controlling Dynamixel Servos

## Slide 10: Dynamixel Servo Family

## Slide 11: Servo Test/Control Setup
USB2Dynamixel
- Make sure the switch on the side is at TTL.
USB Cable Connected to a USB HUB that is connected to a PC.
12V DC
Dynamixel AX12

## Slide 12: RoboPlus
You need to install RoboPlus
We will use the tool called Dynamixel Wizard.

## Slide 13: Dynamixel Wizard – Open a port
Select the port
Click on open port button to establish a connection

## Slide 14: Dynamixel Wizard – Search Servos
Make use 1000000 bps is selected
Click on start search

## Slide 15: Dynamixel Wizard – Search Servos
You can click on stop when it finds the servos or wait until the search ends.
The servo names and ID will appear here
It will start searching for ID numbers
Select the servo and double click on it.

## Slide 16: Dynamixel Wizard – Set ID numbers
Select the value you want to change
Change the ID number and click on apply

## Slide 17: Dynamixel Wizard – Turn on/off a servo
Select torque enable to power on/off the servo
Select on to enable the servo

## Slide 18: Dynamixel Wizard – Set goal position
For testing the servo select goal position
Move the red circle to move the servo.
Before put adding servo to the robot make sure it is in the center position!