## Slide 1
ROS Workshop
-Lecture 2-
Python - Raspberry Pi - Robot Operating System
Husnu Melih Erdogan
Lab Assistant
Intelligent Robotics Lab

## Slide 2: Course Structure
Lecture 1 – (Spring - Week 1 )
  What is ROS?
  Introduction to ROS
    ROS architecture, philosophy, history
  How to install ROS?
  Python basics
  Examples
  Lab Assignment 1
Lecture 2 – (Spring - Week 2)
  Linux Basics
  ROS commands
  Getting familiar with the ROS filesystem
  How to create a ROS package?
  How to build a ROS package?
  How to install released ROS packages?
  How to build packages from source?
  Lab Assignment 2 – Turtlebot Project
Lecture 3 - (Spring - Week 3)
  ROS Nodes Detail
  ROS Topics Detail
  Writing a Publisher and Subscriber
  Lab Assignment 3
Lecture 4 - (Spring - Week 4)
  ROS Services and Messages
  Writing a Service and Client
  ROS .bag file
  Lab Assignment 4
Lecture 5 - (Spring - Week 5)
  URDF
  TF
  Getting started with Turtlebot
  Lab Assignment 5
Lecture 6 - (Spring - Week 6)
  MoveIt
  Creating Vikingbot URDF
  Robot_State_Publisher
  Joint_State_Publisher
  Lab Assignment 6
Lecture 7 - (Spring - Week 7)
  Gazebo
  Creating a Simple Vikingbot Simulation
  Lab Assignment 7
Spring Week 8 - 9 - 10
  Turtlebot - Vikingbot Project

## Slide 3: Linux Cheat Sheet

## Slide 4: Linux – Useful Linux Commands
passwd : change password
ls : Lists the content of the current directory
cd : Changes the current directory to the one specified
pwd: Displays the name of the current working directory
mkdir: Makes a new directory
rmdir: Remove empty directories
nano:
rm: Removes the specified file
cp: Makes a copy of a file and places it at the specified location
mv: Moves a file and places it at the specified location

## Slide 5: Linux – Useful Linux Commands
cmod : Normally used to change the permissions for a file
ssh: Secure shell. Connect to another computer using an encrypted network connection
sudo: Run a command as a superuser, or another user.
unzip : Extracts the files from a compressed zip file.
Ifconfig : Displays the network configuration details for the interfaces on the current system when run without any arguments
sudo shutdown –h

## Slide 6: XML Format
Xml stands for extensible markup language.
<note> <to>Tove</to> <from>Jani</from> <heading>Reminder</heading> <body>Don't forget me this weekend!</body> </note>
The XML above does not DO anything. XML is just information wrapped in tags.

## Slide 7: XML Tags and Elements
https://www.youtube.com/watch?v=nyk8QO08grM

## Slide 8: Why XML?
It simplifies data sharing
It simplifies data transport
It simplifies platform changes
It simplifies data availability
If you want to learn more about xml:
https://www.w3schools.com/xml/default.asp

## Slide 9: Review of Last Week
Rostopic
Rosnode
Messages
Master

## Slide 10: ROS Master, Nodes, Topics
ROS Master
Node 1
Publisher
Node 2
Subscriber
Node 3
Subscriber and Publisher
Registration
Registration
Registration
Topic
Topic
Publish
Publish
Subscribe
Subscribe

## Slide 11: Summary of ROS Messages
Image Source Link

## Slide 12: ROS File System
Packages: Packages are the software organization unit of ROS code. Each package can contain libraries, executables, scripts, or other artifacts.
Manifests (package.xml): A manifest is a description of a package. It serves to define dependencies between packages and to capture meta information about the package like version, maintainer, license, etc...

## Slide 13: rospack
rospack : gives you information about the package
rospack find package_name
ex: rospack find roscpp

## Slide 14: roscd
It is used to change directory to a package or a stack.
  roscd package_name
You can also use roscd to move into sub directories.
  roscd package_name/sub_directory

## Slide 15: rosls
It is used to list to directories inside a package.
  rosls roscpp_tutorials
  Cmake launch package.xml srv

## Slide 16: rosdep
It is used to install system dependencies.
rosdep install my_package
rosdep install --from-paths src --ignore-src --rosdistro indigo

## Slide 17: How to Install ROS Packages?
There are two ways to do it.
If there is a Debian package it is easy to install.
If there is no deb package, you have to install it from by sources.

## Slide 18: ROS Package Review
Software in ROS is organized in packages.
A package can contain your ROS nodes, any libraries, a dataset, configuration files, message types, scripts, service types, some third-party software.
When you want to create a project in ROS, first you need to create a package
ROS package are usally for certain ROS distributions
Packages have dependencies
http://www.ros.org/browse/list.php?package_type=package&distro=indigo

## Slide 19: Method 1
apt-get install ros-<ros-distribution>-<package-name>
Example:
http://www.ros.org/browse/list.php
apt-get install ros-indigo-effort-controllers

## Slide 20: Method 2
- cd catkin_ws/src
- https://github.com/ros/ros_tutorials
- git clone -b indigo-devel https://github.com/ros/ros_tutorials.git
- cd catkin_ws
- rosdep install --from-paths src --ignore-src --rosdistro indigo
- catkin_make

## Slide 21: Server Login
Windows:
  run Putty
Other:
  ssh yourname@ros-server.ece.pdx.edu
Password: SpringROS12345

## Slide 22: Example 1
talker.py
listener.py
Topic: chatter
Msg: String
Topic: chatter
Msg: String

## Slide 23: Example 1
Student 1 : rosrun rospy_tutorials listener.py
Student 2 : rosrun rospy_tutorials talker.py

## Slide 24: Example 2
talker.py
listener.py
Topic: chatter1
Msg: String
Topic: chatter1
Msg: String
talker.py
listener.py
Topic: chatter2
Msg: String
Topic: chatter2
Msg: String
Student 1
Student 2
Student 3
Student 4
talker.py
listener.py
Topic: chatter3
Msg: String
Topic: chatter3
Msg: String
Student 5
Student 6

## Slide 25: Remapping Arguments
Any ROS name within a node can be remapped when it is launched at the command-line.
http://wiki.ros.org/Remapping%20Arguments

## Slide 26: Example 2
Student 3 : rosrun rospy_tutorials listener.py /chatter:=/chatter2
Student 4 : rosrun rospy_tutorials talker.py /chatter:=/chatter2
Student 1 : rosrun rospy_tutorials listener.py /chatter:=/chatter1
Student 2 : rosrun rospy_tutorials talker.py /chatter:=/chatter1
Student 5 : rosrun rospy_tutorials listener.py /chatter:=/chatter3
Student 6 : rosrun rospy_tutorials talker.py /chatter:=/chatter3

## Slide 27: How to Create a ROS Package?
For a package to be considered a catkin package it must meet a few requirements:
The package must contain a catkin compliant package.xml file.
  That package.xml file provides meta information about the package.
The package must contain a CMakeLists.txt which uses catkin. If it is a catkin metapackage it must have the relevant boilerplate CMakeLists.txt file.
There can be no more than one package in each folder.
  This means no nested packages nor multiple packages sharing the same directory.

## Slide 28: ROS Package
Way 1:
Way 2:

## Slide 29: How to Create a ROS Package?
Create your workspace
Go to your source directory
  cd ~/catkin_ws/src
Create a new package
  catkin_create_pkg <package_name> [depend1] [depend2] [depend3]
Build the workspace and source the setup.bash file
  cd ~/catkin_ws
  . ~/catkin_ws/devel/setup.bash

## Slide 30: Rospack Dependencies
catkin_create_pkg beginner_tutorials std_msgs rospy roscpp

## Slide 31: Rospack Dependencies
These dependencies for a package are stored in the package.xml file:

## Slide 32: Indrect Dependencies
A dependency can also have its own dependencies.
All indirect dependencies

## Slide 33: Customize your ROS Package
The generated package.xml should be in your new package.

## Slide 34: Customize your ROS Package
Description Tag:
  Describe your package in a few words

## Slide 35: Customize your ROS Package
Maintainer Tags:
  This is a required and important tag for the package.xml
  Let others know who to contact about the package.

## Slide 36: Customize your ROS Package
License Tags:
  You should choose a license and fill it in here. Some common open source licenses are BSD, MIT, Boost Software License, GPLv2, GPLv3, LGPLv2.1, and LGPLv3

## Slide 37: Customize your ROS Package
Dependencies Tags:
  We define all of our specified dependencies to be available at build and run time.

## Slide 38: ROS Package Review

## Slide 39
TURTLEBOT 2i PROJECT

## Slide 40: Project

## Slide 41: Turtlebot Project
Please check your emails.
Go to the website, watch the videos.
Create a 2D map of the lab.
Team 1 use turtlebot 1,
Team 2 use turtlebot 2.
We will pick the best one and use it in this projects.

## Slide 42: Lab Assignment 2
Create a package in your work space:
  Name the package <yourname>_myf_irst_package
  Dependencies: std_msgs, rospy, roscpp
  Customize your package.