## Slide 1: ECE 478-578 Intelligent Robotics I
PhD. Husnu Melih Erdogan – Electrical & Computer Engineering
herdogan@pdx.edu Teaching Assistant – Lab Assistant

## Slide 2: Lecture 16 Introduction to ROS

## Slide 3: ROS (Robot Operating system)

## Slide 4: Course Structure
  What is ROS?
  Introduction to ROS
    ROS architecture, philosophy, history
  How to install ROS?
  Examples
  XML Format
  ROS commands
  Getting familiar with the ROS filesystem
  How to create a ROS package?
  How to build a ROS package?
  How to install released ROS packages?
  How to build packages from source?
  ROS Nodes Detail
  ROS Topics Detail
  Writing a Publisher and Subscriber
  ROS Services and Messages
  Writing a Service and Client
  ROS .bag file
  URDF
  TF
  RVIZ
  Getting started with Turtlebot
  MoveIt
  Creating Vikingbot URDF
  Robot_State_Publisher
  Joint_State_Publisher
  Gazebo

## Slide 5: What is ROS?
ROS stands for Robot Operating System.
However it is not a real operating system such a Linux, Windows, OSX
It is framework.
It is more like a middleware that sits between your operating system and your program in C++, Python, and Matlab etc.

## Slide 6: Why ROS is useful?
A distributed, modular design
A very large community
Permissive Licensing
  "lets people do anything they want with your code as long as they provide attribution back to you and don’t hold you liable."
Collaborative Environment
It is free.
Supports different programming languages
  Matlap, C++, Python, Lisp
A very important technical skill to have in your resume.

## Slide 7: History of ROS
It is developed in 2007 at the Stanford Artificial Intelligence Lab.
It was managed by Willow Garage.
Open Source Robotics Foundations has been managing it since 2013.

## Slide 8: Current Distributions

## Slide 9: ROS Industrial
http://rosindustrial.org/
ROS-Industrial is an open-source project that extends the advanced capabilities of ROS software to manufacturing.

## Slide 10: Turtlebot

## Slide 11: ROS Philosophy
Peer to Peer
  Individual programs communicate over defined API (ROS messages, services)
Distributed
  Programs can be run on multiple computers and communicate over the network.
Supports Multiple Languages
  ROS modules can be written in any language for which a client library exist (C++, Python, MATLAB, Java, etc.)
Light-weight
  Stand-alone libraries are wrapped around with in a thin ROS layer.
  It doesn’t mean ROS doesn’t use your CPU or don’t need a powerful PC.
  Some packages could use all almost your system resources.
Free and Open-Source
  It is totally free and supported by a considerably large community.
  It is backed by many universities and industrial companies.
  It becomes a standard in the robotics field.

## Slide 12: ROS Core Components
There are three core components:
  Communications Infrastructure
  Robot-Specific Features
  Tools

## Slide 13: Communications Infrastructure
At the lowest level, ROS offers a message passing interface that provides inter-process communication and is commonly referred to as a middleware.
The ROS middleware provides these facilities:
  publish/subscribe anonymous message passing
  recording and playback of messages
  request/response remote procedure calls
  distributed parameter system

## Slide 14: Message Passing
A communication system is often one of the first needs to arise when implementing a new robot application.
ROS's built-in and well-tested messaging system saves you time by managing the details of communication between distributed nodes via the anonymous publish/subscribe mechanism.
Another benefit of using a message passing system is that it forces you to implement clear interfaces between the nodes in your system, thereby improving encapsulation and promoting code reuse.
The structure of these message interfaces is defined in the message IDL (Interface Description Language).

## Slide 15: Recording and Playback of Messages
Because the publish/subscribe system is anonymous and asynchronous, the data can be easily captured and replayed without any changes to code.
Say you have Task A that reads data from a sensor, and you are developing Task B that processes the data produced by Task A. ROS makes it easy to capture the data published by Task A to a file, and then republish that data from the file at a later time.
This is a powerful design pattern that can significantly reduce your development effort and promote flexibility and modularity in your system.
We can run the robot itself only a few times, recording the topics we care about, and then replay the messages on those topics many times, experimenting with the software that processes those data.

## Slide 16: Remote Procedure Calls
The asynchronous nature of publish/subscribe messaging works for many communication needs in robotics, but sometimes you want synchronous request/response interactions between processes.
The ROS middleware provides this capability using services. Like topics, the data being sent between processes in a service call are defined with the same simple message IDL.

## Slide 17: Distributed Parameter System
The ROS middleware also provides a way for tasks to share configuration information through a global key-value store.
This system allows you to easily modify your task settings, and even allows tasks to change the configuration of other tasks.

## Slide 18: Robot-Specific Features
In addition to the core middleware components, ROS provides common robot-specific libraries and tools that will get your robot up and running quickly. Here are just a few of the robot-specific capabilities that ROS provides:
  Standard Message Definitions for Robots
  Robot Geometry Library
  Robot Description Language
  Preemptable Remote Procedure Calls
  Diagnostics
  Pose Estimation
  Localization
  Mapping
  Navigation

## Slide 19: Tools
One of the strongest features of ROS is the powerful development toolset.
These tools support introspecting, debugging, plotting, and visualizing the state of the system being developed.
The underlying publish/subscribe mechanism allows you to spontaneously do self-analysis of the data flowing through the system, making it easy to comprehend and debug issues as they occur.
The ROS tools take advantage of this introspection capability through an extensive collection of graphical and command line utilities that simplify development and debugging.

## Slide 20: Command-Line Tools
ROS can be used 100% without a GUI.
All core functionality and introspection tools are accessible via one of more than 45 ROS command line tools.
There are commands for launching groups of nodes;
  introspecting topics,
  services,
and actions;
  recording and playing back data;
  and a host of other situations.

## Slide 21: rviz
Perhaps the most well-known tool in ROS, rviz provides general purpose, three-dimensional visualization of many sensor data types and any URDF-described robot.
rviz can visualize many of the common message types provided in ROS, such as
  laser scans,
  three-dimensional point clouds,
  and camera images.
Visualizing all of your data in the same application not only looks impressive, but also allows you to quickly see what your robot sees, and identify problems such as sensor misalignments or robot model inaccuracies.

## Slide 22: rviz

## Slide 23: rviz

## Slide 24: rviz

## Slide 25: rviz

## Slide 26: How to Install ROS?
Installing ROS on PC – Ubuntu
Installing ROS on Virtual Machine
Installing ROS on Raspberry Pi 3 - Jessie
Installing ROS on Raspberry Pi – Ubuntu Mate

## Slide 27: ROS Workspace Environment
Standard name for it catkin_ws
You can use whatever name you want.
Check your work space.
First you need to source your setup.*sh.
The setup.bash files setup your environment variables and paths.
source /opt/ros/<distro>/setup.bash
Ex: source /opt/ros/kinetic/setup.bash

## Slide 28: Create a Catkin Workspace
What is catkin?
A catkin workspace is a folder where you modify, build, and install catkin packages. (wiki.ros.org)
Catkin packages can be built as a standalone project, in the same way that normal cmake projects can be built, but catkin also provides the concept of workspaces, where you can build multiple, interdependent packages together all at once.

## Slide 29: Create a Catkin Workspace
- mkdir -p ~/catkin_ws/src
(create a new directory called src in another directory called catkin ws)
- cd ~/catkin_ws/src
( go into the src directory)
- catkin_init_workspace
(initialize the workspace)
cd ~/catkin_ws/
(go into your brand new workspace)
catkin_make
(build your code in a catkin workspace)
source devel/setup.bash
(Before continuing make sure you source your new setup.*sh file)
echo $ROS_PACKAGE_PATH
Test your path: /home/youruser/catkin_ws/src:/opt/ros/kinetic/share

## Slide 30: ROS Master
In charge of managing the communication between nodes
Every node registers with the master when you run them
It tracks publishers and subscribers to topics as well as services.
The role of the Master is to enable individual ROS nodes to locate one another.
Once these nodes have located each other they communicate with each other peer-to-peer.
The Master also provides the Parameter Server.

## Slide 31: ROS Master
In order to start a master type:
  roscore

## Slide 32: Ros Nodes
Single-purpose, executable program written in Python, C++, Matlab etc
Individually complied, executed and managed.
You can run, stop, and kill nodes whenever you want.
They run in parallel.
In order to run a node type:
  rosrun package_name node_name
See active nodes running on ROS
  rosnode list
In order to get more information about nodes type:
  rosnode info node_name

## Slide 33: ROS Master and Nodes
ROS Master
Node 1
Node 2
Node 3
Registration
Registration
Registration

## Slide 34: ROS Master Example
Step 1
Step 2
Step 3

## Slide 35: ROS Topics
ROS Nodes communicate over topics.
Each node can publish or subscribe topics
When one of the nodes register with the master, node also tells master that I am the publisher of these topics. Therefore, other nodes can know who publishes that topic and subtribe that topic.
List all active topics :
  rostopic list
Subscribe and print the contents of a topic
  rostopic echo /topic-name
Show information about the topic
  rostopic info /topic-name
Show all the other possible rostopic commands
  rostopic -h

## Slide 36: Other ROS Topic Commands
rostopic bw display bandwidth used by topic
rostopic echo print messages to screen
rostopic hz display publishing rate of topic
rostopic list print information about active topics
rostopic pub publish data to topic
rostopic type print topic type

## Slide 37: Using rqt-graph
rqt_graph tool is used to create a dynamic graph of what's going on in the system that includes all nodes and topics
To run rqt-graph
  rosrun rqt_graph rqt_graph

## Slide 38: ROS Master, Nodes, Topics
ROS Master
Node 1
Publisher
Node 2
Subscriber
Node 3
Subscriber and Publisher
Registration
Registration
Registration
Topic
Topic
Publish
Publish
Subscribe
Subscribe

## Slide 39: ROS Messages
ROS message describes the data values that ROS nodes publish.
Messages help ROS tolls to automatically generate code for the message type in several target languages.
Message descriptions are in .msg files in the msg/ directory.
Messages can be nested in each other.
Each ROS distribution can have a different description for a message
  You can go to http://wiki.ros.org/msg and check the message type
Publish a message to a subscriber ROS node on command line.
  rostopic pub /mytopic std_msg/String “data: ‘Portland State University’”

## Slide 40: Example ROS Message Definition:

## Slide 41: Message Types
You must not use the names of built-in types or header when constructing your own message types.

## Slide 42: Summary of ROS Messages
Image Source Link

## Slide 43: ROS Package
Software in ROS is organized in packages.
A package can contain your ROS nodes, any libraries, a dataset, configuration files, message types, scripts, service types, some third-party software.
When you want to create a project in ROS, first you need to create a package
You can also download and install many packages written by other ROS users around the world
You can submit the ROS package you write to the ROS package repository
Every ROS package is for certain ROS distributions
Packages have dependencies
http://www.ros.org/browse/list.php?package_type=package&distro=indigo

## Slide 44: ROS Launch
Sometimes you have so many nodes with many different arguments and parameters to run in a project.
Roslaunch is a tool for easily launching multiple ROS nodes as well as setting parameters in the parameter server.
The basic idea is to list, in a specific XML format, a group of nodes that should be started at the same time.

## Slide 45: Example Launch File

## Slide 46: Some useful ROS command-line tools
rospack: find and retrieve information about packages
catkin_create_pkg: create a new package
catkin_make: build a workspace of packages
rosdep: install system dependencies of a package
rqt: In rqt there is a plugin called "Introspection/Package Graph", which visualizes package dependencies as a graph

## Slide 47
Turtlesim Example
http://wiki.ros.org/turtlesim
Roscore
Nodes:
  rosrun turtlesim turtlesim_node
  rosrun turtlesim_turtle_teleop_key
Rostopic:
  rostopic pub -1 /turtle1/cmd_vel geometry_msgs/Twist -- '[2.0, 0.0, 0.0]' '[0.0, 0.0, 1.8]'